## Slide 1
SunMRRC
Software Design Description · V3.5
SunSDR2 DX · Web-Based Mobile Remote Radio Control
16
SDD Chapters
16
Architecture Decisions
5
WebSocket Endpoints
96%
SSB Power Efficiency
4.5/5
TX Audio MOS Score
June 30, 2026 · Target: iPhone iOS Safari · HTTPS/WSS with SharedArrayBuffer

## Slide 2
01. Executive Summary
What SunMRRC is and what changed in V3.5
📡
Purpose
HTTPS/WSS web server providing real-time remote control of SunSDR2 DX transceiver from iPhone/iOS Safari. Features: real-time spectrum waterfall, RX audio streaming (Opus 16kHz), TX voice modulation (Python Hilbert SSB), PTT management, ADIF logbook.
🔄
V3.5 Major Changes
WDSP TX C-chain removed (Python Hilbert sole SSB path). SharedArrayBuffer ring buffer for zero-main-thread TX audio. 300Hz 4th-order Butterworth HPF for 96% SSB efficiency (was 69%). COEP credentialless for Safari Worker compatibility. Continuous DC blocker replacing per-frame subtraction.
✅
Verified Metrics
TX IQ peak=0.69 RMS=0.68 @100% drive. 37dB SNR. Zero frame dropouts across 340 frames. SSB band efficiency 96%. MOS audio quality score: 4.5/5.0. SAB ring buffer: 1.024s @ 16kHz.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 3
02. Architecture Overview
System context, logical flow, RX & TX signal chains
iOS Safari Browser
FastAPI SunMRRC Server
SunSDR2DX Client (UDP)
SunSDR2 DX Hardware
RX Signal Chain (Server Side)
IQ UDP (port 50002) → StreamProcessor → SpectrumProcessor (FFT 2048) → /WSspectrum → AudioDemodulator (SSB/AM/FM + WDSP RX) → Opus Encode → /WSaudioRX WDSP: AGC(SLOW) + NR2(level 50) + NB + ANF S-Meter: GetRXAMeter(ch0, 0) → frontend S-meter
TX Signal Chain (End-to-End)
Mic → AudioWorklet (48k→16k downsampling) → SAB Ring Buffer (16384 float32, lock-free SPSC) → Opus Worker (poll 3ms → Opus 28kbps → WS) → /WSaudioTX → DC Blocker (20Hz IIR) → 300Hz HPF (4th-order Butterworth) → Anti-alias LPF (3.6kHz 4th-order BW) → Resample 16k→15625 → Python Hilbert SSB → Drive Gain ×2.8 → tanh Limiter → 24-bit IQ Encode → UDP 0xFFFD → Device
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 4
03. Component Model
Key modules and their roles
Server + WebSockets
sunmrrc/server.py
FastAPI, lifespan, 5 WS, IQ loop, audio/spectrum broadcast, COOP/COEP middleware, pre-bound IQ socket, dedicated keep-alive thread.
Radio Client
web_control/sunsdr_direct.py
SunSDR2 DX UDP protocol: boot, heartbeat (0x0018), freq/PTT/AGC, DRIVE (0x0017) with sqrt taper.
DSP Pipeline
web_control/dsp.py
StreamProcessor → SpectrumProcessor (FFT 2048) + AudioDemodulator (SSB/AM/FM + WDSP RX). TX: TXModulator with Python Hilbert SSB, 300Hz HPF, tanh limiter. WDSP RX-only.
Frontend
sunmrrc/static/
controls.js (WS+audio+waterfall), mobile.js (UI), tx_capture_worklet.js (SAB producer), tx_opus_worker.js (SAB consumer+Opus+WS).
WDSP Wrapper (RX-only)
web_control/wdsp_wrapper.py
Optional libwdsp.dylib ctypes. Ch0=RX audio (AGC,NR2,NB,ANF). Ch1=RX IQ (IF-SDR). WDSP TX C-chain (ch2) removed V3.5.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 5
04. TX Audio Chain — SAB Ring Buffer
Zero-main-thread: AudioWorklet → SharedArrayBuffer → Opus Worker → WebSocket
Microphone 48kHz
AudioWorklet 48k→16k float32
SAB Ring Buffer 16384 float32 1.024s @ 16kHz Lock-free SPSC
Opus Worker Poll 3ms Opus 28kbps Own WebSocket
/WSaudioTX Tagged frames 0x01=Opus 16kHz
SAB Ring Buffer Design
Layout: word[0]=write_pos (U32), word[1]=read_pos, word[2+]=float32[16384] (power-of-2 for fast &) Producer (AudioWorklet): process() @ 128 samples/48kHz quantum 3:1 box-average decimation → 160@16kHz writeRing(samples,n) → Atomics.store(writePtr) Consumer (Opus Worker): setInterval(pollSAB, 3ms) sabAvailable() → sabRead(320) → encodeAndSend COOP/COEP: credentialless (not require-corp) Safari importScripts() compat for Opus WASM Fallback: postMessage Int16Array if no SAB
Key Design Decisions
1. Zero main-thread path → GC pauses cannot stall TX audio stream 2. Lock-free SPSC via Atomics — no mutex, no postMessage overhead for audio samples 3. 1.024s buffer depth — survives worst-case 287ms browser GC pause (logged in prod) 4. Worker-owned WebSocket — main thread never touches /WSaudioTX in SAB path 5. COEP credentialless + CORP cross-origin headers ensure Safari compat 6. SAB sent BEFORE start message to Worker — startPolling() always has _sab ready
SunMRRC SDD V3.5 · TX Audio Chain · SAB Ring Buffer Path

## Slide 6
05. TX Signal Processing Pipeline
10 stages — from Opus-decoded PCM to 24-bit IQ packets
0 Opus Decode
1 DC Blocker 20Hz IIR
2 300Hz HPF 4th-order
3 Anti-alias LPF 3.6kHz
4 Resampler 16k→15625
5 Hilbert SSB
6 Drive Gain ×2.8
7 tanh Limiter
8 Amplitude Ramp
9 24-bit Encode
Filter Specifications
DC Blocker (Stage 1): H(z)=(1-z⁻¹)/(1-R·z⁻¹), R=exp(-2π·20/fs) First-order IIR, continuous state across calls Replaces per-frame x-=x.mean() — removed clicks at 76% of 20ms frame boundaries 300Hz HPF (Stage 2): ★ NEW in V3.5 4th-order Butterworth, SOS topology Reduces sub-300Hz: 30.4% → 3.7% of total SSB band efficiency: 69% → 96% Reclaims ~15% PA headroom Anti-alias LPF (Stage 3): 4th-order Butterworth @ 3.6kHz Prevents 7.8+ kHz folding into voice band
Modulation & Level Control
Python Hilbert Overlap-Save (Stage 5): scipy.signal.hilbert() on 592-sample blocks 80-sample hop, 256-sample margin each side Phase-continuous (0.20 rad jumps vs WDSP 1.24) USB / LSB / AM mode support Drive Gain & tanh Limiter (Stages 6-7): TX_DRIVE_GAIN = 2.8 (tuned 3.0→3.5→2.8) TX_IQ_PEAK = 1.0 (fixed soft-limit ceiling) tanh(mag/ceiling)×ceiling — smooth saturation Peak IQ: 0.69, RMS: 0.68 @100% drive Amplitude Ramp (Stage 8): 200-sample cosine fade-in/out Prevents hard transients on PTT assert/release 24-bit LE IQ Encode (Stage 9): 200 IQ × 6 bytes = 1200 bytes/packet Packed as 24-bit signed LE ints
SunMRRC SDD V3.5 · TX Signal Processing · 10-Stage Pipeline

## Slide 7
06. WebSocket Endpoints
5 endpoints — bidirectional text, binary streaming, JSON proxy
/WSCTRX
Bidirectional text
Control: setFreq, setMode, setPTT, setDrive, setSampleRate, getWDSPStatus (RX-only), band/memory APIs. Broadcast to all ctrl_clients.
/WSaudioRX
Server→Client binary
RX audio. 1-byte codec tag: 0x00=PCM 16kHz, 0x01=Opus 16kHz mono (~18-24kbps). Default Opus. Falls back to PCM if libopus missing.
/WSaudioTX
Client→Server binary
TX audio uplink. Opus-encoded from dedicated Worker-side WS (SAB path). Tag 0x01=Opus. Text: m: metadata, s: stop. Server ctypes Opus decoder. TX capture on PTT release.
/WSspectrum
Server→Client binary
512 uint8 dB rows. 0=-120dB, 255=0dB. Server-side quantized. 512 B/frame @ 10Hz = 5KB/s.
/WSATR1000
Bidirectional JSON
ATR-1000 tuner proxy (placeholder). Accepts connections. No hardware interface yet.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 8
07. TX Power & Drive (0x0017)
Device drive control, IQ gain staging, and telemetry
DRIVE Command (0x0017)
Byte: round(255×√(drive%/100)) — sqrt taper 10%→0x50, 50%→0xb4, 100%→0xff Packet: drive byte in TRAILING word, NOT payload build_packet(DRIVE, data=b"", trailing=byte) Re-sent on every QSY + PTT assert Device resets to per-band calibration otherwise Per-band power: band_power.json + /api/band_power Frontend Band Power menu panel
IQ Gain Staging
TX_IQ_PEAK = 1.0 (verified vs ExpertSDR3) TX_DRIVE_GAIN = 2.8 (tuned 3.0→3.5→2.8) Client: AudioTX_preamp = 1.5 (+3.5dB) Reduced from 3.0 to avoid Int16 saturation 300Hz HPF: reclaims ~15% PA headroom Filters subsonic energy before gain stages IQ amplitude CONSTANT with drive % Drive only scales RF power at device PA
TX Power / Voltage Telemetry (0x1F00, 34 bytes)
Reverse-engineered 2026-06-25 from expert_40m_drive.pcap (full 40m drive sweep): off30 f32 Forward Power (PEP) in WATTS — direct float, no fit needed off22 f32 Average forward power (ratio to off30 ≈ SSB crest factor 3:1) off16 u16 Supply voltage × 10 (~13.6V idle, sags under load, correlation with power=-0.79) off18 f32 PA temperature °C (~42°C, barely moves) off26 f32 Always 1.0000 (device placeholder) Frontend getTXTelem: watts, volts, temp. NO SWR — device has no reverse-power field. Old off14 "power" was non-monotonic noise. Old off16/100 "SWR" was actually supply voltage.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 9
08. PTT Safety Architecture
Multi-layer defense against stuck transmitter
Layer 1
ACK Retry
Frontend retries setPTT:true up to 3 times. If no ACK, does NOT stream audio.
Layer 2
Watchdog Timer
Frontend 3-second watchdog. If no heartbeat during TX, auto-releases PTT.
Layer 3
Forced-RX Handler
Server s: handler: clears PCM queue, resets modulator, calls radio.set_ptt(False).
Layer 4
TX Pacer Timeout
TX IQ pacer stops on PTT de-assert. tx_thread_stop flag + join(1.0s).
Layer 5
Device Watchdog
SunSDR2 DX firmware: kills TX after ~3s silence. Hardware-level safety net.
All PTT safety layers operate at WebSocket command level — independent of DSP modulation path. WDSP TX C-chain removal has no bearing on PTT safety.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 10
09. WDSP Integration (RX-Only)
libwdsp.dylib — AGC, NR2, NB, ANF for receive path. TX C-chain removed.
RX Audio Channel (ch0) @ 16kHz
OpenChannel(type=0, RXA): buffer=256, rate=16000 Chain: AGC(SLOW) → NR2(level 50, AE zeta/psi) → NB(opt) → ANF(opt) → BP(200-3400Hz) → EQ(10-band graphic) NR2: zeta 0.50→0.08, psi 0.01→0.08 (SetRXAEMNRgainLine does NOT exist in build) S-Meter: GetRXAMeter(ch0, 0) → double restype=c_double critical for ARM64
RX IQ Channel (ch1) @ 78125Hz
OpenChannel(type=0, RXA): buffer=1024, rate=78125 IF-SDR: NR2/ANF on full-rate I/Q before demod → WDSP demodulates at IQ rate → Python [::5] decimation to 15625Hz → Anti-alias bandpass 200-3400Hz fexchange0 on interleaved I/Q: [I0,Q0,I1,Q1,...] Output ratio calibrated on first block (~0.200) Spatial diversity (fexchange2) placeholder — dual-ADC streaming not yet confirmed on SunSDR2
WDSP Commands (RX-only, via /WSCTRX)
Enabled: setWDSPEnabled | NR2: setWDSPNR2 (0-100) | AGC: setWDSPAGC (OFF/0..FAST/4) | NB: setWDSPNB | ANF: setWDSPANF NF: setWDSPNF | Squelch: setWDSPSquelch(dB) | Notches: addWDSPNotch | EQ: setWDSPEQ | AGC params: Attack/Decay/Hang (ms) Query: getWDSPStatus → JSON (RX state — no TX chain state returned) TX C-chain commands (setWDSPTXEnabled, setWDSPDEXP, setWDSPCFC, setWDSPLeveler, setWDSPALC, setWDSPTXEQ, setWDSPCFCPrecomp, setWDSPDEXPThresh) — REMOVED in V3.5. Python Hilbert is sole SSB modulation path. WDSP is optional — demods work without it; get_wdsp_status() reports available: true/false.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 11
10. Architecture Decisions Summary
16 ADs with rationale
AD-001
FastAPI over Tornado
Modern async, WS native
AD-002
Direct UDP over TCI
Lower latency, no TCI overhead
AD-003
Mode is DSP-owned
Hardware mode-agnostic
AD-004
RX dual-codec
Opus+PCM fallback, 1-byte tag
AD-005
Spectrum server quantized
512 uint8; 5KB/s mobile BW
AD-006
HTTPS/WSS required
iOS Safari getUserMedia
AD-007
PTT multi-layer safety
ACK+watchdog+forced-RX+HW
AD-008
WDSP is optional
Demods work without libwdsp
AD-009
TX SSB modulation
Python Hilbert (sole path V3.5)
AD-010
Per-band TX power
band_power.json, sqrt drive
AD-011
Opus TX encoding
28kbps CBR, ctypes decoder
AD-012
TX gain staging
Preamp×1.5 + Drive×2.8 + HPF
AD-013
WDSP TX C-chain removed
fexchange0 ch2=zero output
AD-014
SAB Ring Buffer for TX
Zero-main-thread audio path
AD-015
300Hz HPF for SSB
69%→96% band efficiency
AD-016
COEP credentialless
Safari Worker importScripts compat
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 12
11. TX Audio — Verified Performance Metrics
End-to-end SDR pre-modulation analysis results
IQ peak @100% drive
0.69
IQ RMS @100% drive
0.68
Signal-to-Noise Ratio
37 dB
SSB band efficiency
96%
Frame dropouts
0
Sub-300Hz (post-HPF)
3.7%
Crest factor (100ms)
11.3 dB
DC offset (carrier leak)
-99 dBc
TX uplink jitter std
0.9 ms
Frame interval mean
23.5 ms
MOS audio quality
4.5 / 5.0
SAB ring buffer
1.024 s
Source: post-DC-block WAV analysis (post-HPF) + TX uplink CSV jitter analysis · June 2026
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 13
12. Known Gaps & Roadmap
Implemented vs. planned
✅
TX SSB Modulation
Python Hilbert overlap-save. Verified: 37dB SNR, 96% efficiency, 0 dropouts. SAB ring buffer active.
✅
Per-band TX Power
band_power.json, /api/band_power, Band Power menu. DRIVE 0x0017 sqrt mapping verified.
✅
TX Power Telemetry
0x1F00: off30=f32 watts PEP, off16=u16/10 volts, off18=f32 temp. No SWR (no reverse-power HW).
✅
300Hz HPF
4th-order Butterworth. SSB efficiency 69%→96%. Post-HPF verified: sub-300Hz=3.7%.
🔄
Sample Rate Selector
39/78/156/312kHz via 0x0001 HW_INIT word[11]. Frontend menu. Full re-boot required.
⏳
ATR-1000 Tuner
/WSATR1000 accepts connections; no hardware interface yet.
⏳
Memory Channels
/api/mem_channels GET/POST + JSON persistence. UI needs polish.
⏳
WDSP TX Re-eval
Removed V3.5 (zero IQ). Could revisit if libwdsp build confirmed TXA-compatible.
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 14
13. Version History
SDD evolution V3.0 → V3.5
V3.0
2026-06-21
Initial SDD: 12 chapters, 8 ADs, system context, component model
V3.1
2026-06-23
PTT safety (AD-007), WDSP optional (AD-008), TX SSB modulation (AD-009)
V3.2
2026-06-24
Per-band power (AD-010), Opus TX (AD-011), TX gain staging (AD-012)
V3.3
2026-06-26
TX power telemetry (0x1F00) reverse-engineered
V3.4
2026-06-28
TX telemetry field corrections. Architecture diagrams.
V3.5
2026-06-30
★ WDSP TX removed (AD-013). SAB ring buffer (AD-014). 300Hz HPF (AD-015). COEP credentialless (AD-016). Continuous DC blocker. Pre-bound IQ socket. Keep-alive thread. TX verified: IQ peak=0.69, 37dB SNR, 96% efficiency, 0 dropouts.
Current: V3.5 (June 30, 2026) · 16 ADs · 16 SDD Chapters
SunMRRC SDD V3.5 · SunSDR2 DX Mobile Remote Control · June 2026

## Slide 15
SunMRRC
Software Design Description · V3.5
SunSDR2 DX Web-Based Mobile Remote Radio Control 16 Architecture Decisions · 16 SDD Chapters · 5 WebSocket Endpoints TX Verified: 37dB SNR · 96% SSB Efficiency · Zero Dropouts
4.5/5
MOS Audio Quality Score
96%
SSB Power Efficiency
37dB
Signal-to Noise Ratio
0
Frame Dropouts
16
Architecture Decisions
June 30, 2026 · github.com/cheenle/sunsdr